## Slide 1: Platte River Recovery Implementation Program ISAC Report to Governance Committee Feedback on Feb. 20-22, 2024 Science Plan Reporting Session June 11, 2024
David Marmorek, ESSA Technologies Ltd, co-chair
Jennifer Hoeting, Hoeting Consulting, co-chair
David Galat, Coop. Assoc. Prof. Retired, University of Missouri
Alan Kasprak, North Rim Research LLC
Aaron Pearse, USGS
Michal Tal, independent consultant
Notes: Good afternoon. I’m Dave Marmorek, co-chair of the Independent Science Advisory Committee (ISAC) together with Jennifer Hoeting. I’m going to summarize the ISAC’s feedback on the Science Reporting Session held February 20 to 22. Several ISAC members are attending virtually and may want to add some comments at the end, or in response to your questions. Before I begin, I’d like to make some general comments on three topics: 1) background on the ISAC; 2) the process we used for this review; and 3) what makes independent science review of Programs work well.
First, the longevity and background of ISAC members: –
I have chaired or co-chaired the ISAC since 2009. I’m an aquatic ecologist with a focus on AM, modeling and decision analysis.
Jennifer Hoeting, the co-chair of the ISAC, joined in 2014; she is an ecological statistician, and is in Indonesia, so not on the call today.
David Galat has been on the ISAC since 2009. He is an expert in large river ecology and restoration, fish ecology and AM.
Alan Kasprak, who joined in July 2023, works on understanding physical and biological processes in rivers using field work, modeling and remote sensing.
Aaron Pearse, who joined in 2022, is a wildlife biologist focusing on the ecology and management of migratory birds, including whooping cranes.
Michal Tal, who joined in 2022, is a fluvial geomorphologist with a special focus on riparian vegetation and channel morphology. It’s after midnight in France, so Michal can’t attend.
Second, the process the ISAC went through for this review. – For the February SPRS, we reviewed 22 documents prior to the meeting in Omaha, listened attentively and asked questions during two days of meetings, responded in writing to 21 separate questions and provided the EDO with 12 additional documents containing our detailed comments on specific reports (including the State of the Platte Report). We used a divide and conquer approach. For example, Michal and Alan addressed sediment augmentation; the two Davids focused on pallid sturgeon. We jointly edited Google Docs with our comments, and had conference calls to resolve outstanding issues.
Third, what makes for effective independent science review? Effective independent science review of programs relies on two things: 1) the independent reviewers understand very well the details of the program; and 2) the program responds to the recommendations of the independent reviewers. Regarding #1, the ISAC has done our very best to understand what the Platte program is doing. However, we aren’t omniscient. We welcome corrections to any misunderstandings we have, through conversations or written feedback. Regarding #2, how the Program responses to ISAC recommendations, that’s up to the program. Over the past 15 years, many ISAC recommendations were adopted by the Program, and led to important improvements. We hope that continues.

## Slide 2: Making science relevant to decisions
Scientists
Uncertainties
Evidence
Experimental design
Models / Tools
Decision Makers
Agency mandates; stakeholders
Management decisions
Risks
Costs and Benefits – did mgmt. action achieve objectives?
Budgets
Hypotheses
Notes: How do you make science relevant to decisions? On the left side of this figure (pink circles) are decision makers like the GC, thinking about… [read clouds, starting w mgmt. decisions and going clockwise]. On the right side (yellow circles) are the scientists, like the TAC and EDO, thinking about… [read clouds, starting w uncertainties, and going clockwise]. In the middle is a bridge between the two worlds.
Bridging these two worlds involves mutual understanding. Decision makers can keep scientists relevant to their decisions and stakeholder tradeoffs, so that applied science provides useful information for decisions. Scientists can keep managers honest, so that they truly understand what can and cannot be accomplished, and what is both known and knowable.
We’ve organized our presentation to bridge these two worlds. The presentation gives a few highlights to stimulate discussion. Our report has a lot more detail.

## Slide 3: Questions posed to ISAC - 1
Questions about the SoPR (simplified)
Q1: Do format and content of 2024 SoPR appropriately communicate Program progress toward addressing EBQs for intended audience (primarily GC)?
Q2: Are 2024 EBQ assessments logical? If not, why not? Respond to Q2 for each of 10 EBQs.
Q3: Does 2024 SoPR provide appropriate support / foundation / justification for key ideas and conclusions?
Q4: Is the Program implementing Extension Science Plan management actions, research, monitoring, data analysis and synthesis in a way that facilitates EBQ assessment throughout the Extension?
Other Questions (simplified)
Q5. Are approaches for evaluating effectiveness of germination suppression flow releases appropriate for quantifying costs and benefits? Should we consider other approaches?
Q6. Are conclusions regarding factors that impact WC roost site selection within AHR well-supported (data, methods, analyses, models), as detailed in WC Roost Site Selection Technical Report? Is the report appropriate for publication?
Q7. Pallid sturgeon: a) Worth collecting data upstream of the Elkhorn River for EBQ#7? b) Is understanding of factors associated with immigration/occurrence and emigration into/out of lower Platte River (LPR) enough to inform Program water management in the central Platte River? c) What will Program learn about pallid sturgeon movement into, through, and out of LPR? d) Does larval trawling at Platte / Missouri confluence help to answer EBQ#7? Should Program maintain larval trawling?
Q8. Piping plovers. a) Are approaches for evaluating effectiveness of predator management appropriate? b) Regardless of management effectiveness, is it worth continuing camera work beyond 2024?
Notes: Our report responds to all the questions posed to the ISAC, summarized here. Altogether there were 21 questions, which had some redundancy. ISAC Q2 (with yellow highlight, under Questions about the SoPR) asked us to review the treatment of each of the 10 EBQs in the SoPR (red text). The “Other Questions” on the bottom half of this slide take a deeper dive into topics related to each EBQ. To reduce redundancy for this presentation, we’ve melded our key conclusions for each EBQ under ISAC Q2 with our related responses to the “Other Questions”.

## Slide 4: Format, Content, Reasoning of SoPR
Decision Makers’ Needs | ISAC Comments & Recommendations
1. Clear, concise, unbiased reports on Program performance for multiple audiences | 1a. Great to see the SoPR! Appropriate format and content. Broaden audience by including Program overview at start.
Notes: The ISAC was asked what we thought of the format, content and reasoning of the SoPR. That’s important because decision makers need… Read decision makers’ needs.
Overall, the ISAC was pleased to see the State of the Platte Report – the first one in five years. We support having State of the Platte Reports every second year. This keeps the GC (and others) in the loop and allows the EDO to provide evidence of recent progress
We have five comments or recommendations on this topic. First (comment 1a), The SoPR has an appropriate format and content for the GC and is well written. Audiences beyond the GC will need a Program overview at the start of the document.

## Slide 5: Format, Content, Reasoning of SoPR
Decision Makers’ Needs | ISAC Comments & Recommendations
2. Concise, credible assessments of progress on Extension Big Questions that synthesize what’s been learned to help with management decisions. | 2a. Acknowledge factors outside Platte which may contribute to observed trends in PPs and WCs
Notes: Read decision makers’ needs. “The GC needs…” We have four general comments regarding this issue.
2a. The SoPR does an excellent job of synthesizing evidence and simplifying the story. We found however that positive trends in habitat or species indicators tend to be attributed primarily to Program actions. Factors outside the Platte may also contribute to observed trends (e.g., rangewide increases in PP and WCs may cause local increases in abundance).

## Slide 6: Format, Content, Reasoning of SoPR
Decision Makers’ Needs | ISAC Comments & Recommendations
2. Concise, credible assessments of progress on Extension Big Questions that synthesize what’s been learned to help GC with management decisions. | 
 | 2b. Rephrase EBQ 1, 2, 4-7 so they’re answerable with thumbs up / down., and reference management hypotheses.
Current EBQ #5. What factors influence WC stopover length within the AHR?
Revised EBQ #5. Does flow influence WC stopover length within the AHR?
Management Hypothesis: Length of WC stopover is a function of discharge.
Notes: 2b. Only one of the Extension Big Questions (EBQ #3) is clearly answerable with a thumbs up / thumbs down approach. We recommend rephrasing the other EBQs so that this useful approach can be applied, AND clearly indicating what management hypotheses are associated with each EBQ. The bottom of this slide shows an example rephrasing for EBQ #5, plus the associated management hypothesis. The current form of EBQ #5 is {read}. That question can’t be answered with a thumbs up / thumbs down approach. You could revise the wording to {read top purple box} and provide a summary response to the management hypothesis which elaborates on all factors affecting stopover length.

## Slide 7: Alternative Phrasing of EBQs for and
Current EBQs | Possible Alternative Phrasing of EBQs
EBQ-1. How effective is it to use Program water to maintain suitable WC roosting habitat? | Can the use of Program water maintain suitable WC roosting habitat?
EBQ-2. How effective is Program management of Phragmites for maintaining suitable whooping crane roosting habitat? | Is the Program effective in managing Phragmites for maintaining suitable whooping crane roosting habitat?
EBQ-4. What factors influence WC decision to stop or fly over the AHR? | Does flow influence WC decisions to stop or fly over the AHR? What other factors are important?
EBQ-5. What factors influence WC stopover length within the AHR? | Does flow influence stopover length within the AHR? What other factors are important?
EBQ-6. Why is spring WC use of the AHR greater than fall WC use? | Is spring WC use of the AHR greater than fall WC use due to higher flows in the Spring? What other factors are important?
EBQ-7. What effect do Program flow management actions to benefit WC, PP, and LT in the central Platte River have on pallid sturgeon use of the lower Platte River? | Does Program flow management affect pallid sturgeon use of the lower Platte River?
EBQ-3 is fine as is. EBQ-8, 9 and 10: “Did we accomplish the stated learning objectives for …”
Notes: This table shows six EBQs on the left. We understand that the GC wanted the EBQs to include non-flow factors. However, a question which begins with “How effective”, “What factors”, “Why” or “What effect” {point to left column} can’t be answered with thumbs up or down. Some possible alternative phrasings of the EBQs, which can more easily be answered with thumbs up or down are shown in the right column. Follow-up questions (in italics) cover other factors.

## Slide 8: How to best summarize “effectiveness”, or “relative importance of different factors”?
Factor | Very Unlikely | Unlikely | Possible | Likely | Very Likely
Factor A |  |  |  |  | 
Factor B |  |  |  |  | 
Factor C |  |  |  |  | 
Factor D |  |  |  |  | 
Factor E |  |  |  |  | 
How likely is it that each of five factors affects… [channel widths], [WC stopping], [WC length of stay]?
Effectiveness at maintaining suitable WC channel widths
Inundation flow magnitude and duration
Poor
Great
OK
Without herbicide
Without herbicide
Hypothetical graph!
Notes: At the June 11 GC meeting, some GC members said that they liked the form of the EBQs, looking at effectiveness and the relative importance of different factors. They were OK to not have a question amenable to thumbs up / thumbs down answers. That begs the question about what forms of summarizing science would be most helpful for the GC in the SoPR. Here are a couple of approaches that could be used. Explain graph and table.

## Slide 9: Format, Content, Reasoning of SoPR
Decision Makers’ Needs | ISAC Comments & Recommendations
2. Concise, credible assessments of progress on Extension Big Questions that synthesize what’s been learned to help GC with management decisions. | 
 | 2c. Continue to apply Structured Decision Making (SDM) to adjust management based on learning, as done in first increment.
Notes: 2c. The ISAC recommends applying SDM (Structured Decision Making) during the Extension, in anticipation of the Second Increment. For example, an SDM exercise could integrate assessments of the relative benefits and costs of different actions in reducing Phragmites (inundation flows, mechanical mgmt. and herbicide), and the best way to combine these actions.
=======

## Slide 10: Format, Content, Reasoning of SoPR
Decision Makers’ Needs | ISAC Comments & Recommendations
2. Concise, credible assessments of progress on Extension Big Questions that synthesize what’s been learned to help GC with management decisions. | 
 | 2d. Test management hypotheses using contrasts in actions over space as well as time.
Notes: 2d. The Extension only spans a decade or so, which isn’t a long time in the big picture of river processes. So it’s important to test hypotheses over space as well as time, looking at an array of channel reaches, segments, or even individual braids of the Platte to get useful contrasts.

## Slide 11: Using Program water to maintain channel widths (1)
Decision Makers’ Needs | ISAC Comments & Recommendations
EBQ #1. How effective is it to use Program water to maintain suitable WC roosting habitat? | 1a. Assess if AHR “habitat-limited” or “crane-limited”.
Fig.10 in SoPR
Notes: Now I’ll move on to each of the EBQs. Read EBQ #1. Water is scarce and expensive. Managers want to use it as effectively as possible to help maintain habitat for WCs. How cost-effective is water compared to other tools in the toolbox like mechanical management and herbicide in maintaining channel widths? How do these tools best work together?
The ISAC had three points to make on EBQ #1. First, it’s worth exploring whether the AHR habitat-limited or crane-limited. Species at risk are often limited more by survival rates than habitat. There could be plenty of WC habitat available in the AHR for more WCs, but there aren’t yet enough birds to occupy this available habitat. The adjusted proportion of WC population (shown at lower left) varies considerably from year to year in both spring and fall, but there isn’t a clear upward trend. WC use of the AHR may be growing proportionally with the overall WC population and WC habitat may not be limiting.

## Slide 12: Using Program water to maintain channel widths (2)
Decision Makers’ Needs | ISAC Comments & Recommendations
EBQ #1. How effective is it to use Program water to maintain suitable WC roosting habitat? | 
 | 1b. Consider multiple factors affecting channel width: year to year variation in natural flow; inundation flows; mechanical mgmt.; herbicide. What’s relative importance of each factor?
Fig. 1 in SoPR
Notes: 1b. Multiple factors affect channel width - year to year variation in natural flow; inundation flows; mechanical mgmt.; herbicide. Knowing the relative importance of each factor and how these factors interact, can help with the GC decide how to allocate money and staff resources. The machine learning model includes all of these factors, which is great. The model might be helpful in elucidating the relative importance of each factor and the variability across reaches, which could help to guide management decisions. The mean TUCW over the entire AHR (the green line on the figure at the lower right) may hide spatial variation that helps to reveal the relative importance of each factor. We suggest looking at what factors correlate with the % of each river segment with MUCW > 650 ft.

## Slide 13: Using Program water to maintain channel widths (3)
Decision Makers’ Needs | ISAC Comments & Recommendations
EBQ #1. How effective is it to use Program water to maintain suitable WC roosting habitat? | 
 | 1c. Clarify use of different channel width metrics: UOCW, TUCW, MUCW. What are the appropriate targets for MUCW? Assess tradeoffs of different types of errors.
Fig. 1 in SoPR
Notes: 1c. The various metrics of channel width have different attributes and uses (say the three metrics). The SoPR should clarify why it uses each metric in each analysis. What are the appropriate targets for MUCW? Many roosts (about 36%) occur in areas with unobstructed channel widths less than 650’. The key management decision is what actions most cost-effectively maintain target channel widths. That decision needs to balance the risks of not maintaining high quality habitat against the risk of wasting money on building very wide channels that aren’t required.

## Slide 14: Using Program water to maintain channel widths (4)
Appendix 3 of WC Roost Site Selection Report
Available channel widths
Channel widths at roosts
Over to Jennifer
Notes: JENNIFER TO DISCUSS SLIDE
Here’s a bit more detail on the issue of targets for UOCW. The blue bars on the left graph show the percent of available channels with different unobstructed channel widths, and the green bars show the percent of channel widths occupied with WC roosts. You can see that there are lots of very narrow channels that aren’t used (tall blue bars and short green bars at the far left). The channel widths with the most roosts are in the middle, at about 600’ to 900’ wide.
** What proportion of each bar in the plot is managed by the program? Want to know for both the available and roost sites.
The answer to this question can help the Program determine the level of impact PRRIP can have on the unobstructed channel widths throughout the AHR.
____________________________________________________________________________________________________________________
(Jennifer omitted Alan’s graph because EDO’s model in doc 8 is a better version of this same idea.)
Alan Kasprak of the ISAC thought it would be interesting to calculate the ratio of these two metrics as a measure of WC selection, which is what you see on the right side. WC relative selection increases up to about 1300’, and then drops off. This is another way of thinking about WC roost selection which might be useful to the EDO and TAC.

## Slide 15: Managing Phragmites to maintain WC habitat (1)
Decision Makers’ Needs | ISAC Comments & Recommendations
EBQ #2. How effective is Program mgmt. of Phragmites for maintaining suitable WC roosting habitat? | 2a. Will 2025 evaluation address past inconsistencies in herbicide application, and consequences for assessing effectiveness? How to resolve in future?
Chapman; October 2023
Notes: Moving on to EBQ #2 (read). As for maintaining channel widths, the GC wants to know how to best combine all tools in the Program toolbox to control Phragmites in the most cost-effective manner.
2a. One of the challenges in answering EBQ #2 is that herbicide has not been consistently applied in the past. It’s hard to know which areas have been treated and which have not. The 2025 evaluation will need to address that problem, and hopefully resolve it for the future.

## Slide 16: Managing Phragmites to maintain WC habitat (2)
Decision Makers’ Needs | ISAC Comments & Recommendations
EBQ #2. How effective is Program mgmt. of Phragmites for maintaining suitable WC roosting habitat? | 
 | 2b. Clarify to everyone that management objective is maintaining channel widths, not increasing them.
Chapman; October 2023
Notes: 2b. Everyone involved needs to understand that inundation flows may maintain channel widths, but cannot increase them. Scouring Phragmites is impossible based on past work funded by the Program - lab experiments and field work by Natasha Bankhead of Leeds University (published in 2016).

## Slide 17: Managing Phragmites to maintain WC habitat (3)
Decision Makers’ Needs | ISAC Comments & Recommendations
EBQ #2. How effective is Program mgmt. of Phragmites for maintaining suitable WC roosting habitat? | 
 | 2c. Simultaneously assess relative effectiveness of inundation flows, mechanical mgmt. and herbicide [all parts of Program management].
Chapman; October 2023
Notes: 2c. It’s important to simultaneously assess the relative effectiveness of all actions to control Phragmites. Is one approach more effective than another? Are there situations where dewatering of vegetation is preferable to inundation flows? What is the relative benefit of each action? We understand that doing this work is part of the data analysis plan for herbicide polygons, which is great.

## Slide 18: Managing Phragmites to maintain WC habitat (4)
Decision Makers’ Needs | ISAC Comments & Recommendations
EBQ #2. How effective is Program mgmt. of Phragmites for maintaining suitable WC roosting habitat? | 
 | 2d. Take advantage of spatial contrast in the level of inundation, using variation in channel widths, morphology, and tributary inputs. Think more about flow split at Rowe Sanctuary.
Chapman; October 2023
Notes: 2d. The management hypothesis is that channel inundation flows of 1,500 cfs are an effective way to reduce Phragmites. A second hypothesis is that channel drying (as occurred at Chapman in September 2023) is also an effective way to reduce Phragmites. A third hypothesis is that channel drying has only a temporary benefit, and that seeds lead to propagation of Phragmites during the next inundation. Using spatial contrasts, as the Program is doing, will be helpful to disentangle these hypotheses.
We recommend further investigating the flow split between the main channel and the north channel upstream of Rowe Sanctuary. It’s worth exploring whether the proposed berm is the most effective way to increase discharge at Rowe.

## Slide 19: Sediment augmentation to maintain WC habitat (1)
Decision Makers’ Needs | ISAC Comments & Recommendations
EBQ #3. Is sediment augmentation necessary to create and/or maintain suitable WC habitat? | 3a. Data synthesis report is excellent. Will be even better after peer review.
Notes: Read EBQ #3: The GC would like to know when and where sediment augmentation is required, how much sediment is required, and the most cost-effective methods of delivering that sediment. The GC also wants to learn what happens without sediment augmentation.
The data synthesis report is excellent, and will be even better after peer review.

## Slide 20: Sediment augmentation to maintain WC habitat (2)
Decision Makers’ Needs | ISAC Comments & Recommendations
EBQ #3. Is sediment augmentation necessary to create and/or maintain suitable WC habitat? | 
 | 3b. Where specifically does Program want to maintain suitable WC habitat? Along the J2 channel? Downstream of Overton? Both?
Notes: 3b. Point to map… Where specifically does Program want to maintain suitable WC habitat? Along the J2 channel? Downstream of Overton? Both reaches? How much risk is the GC willing to take that WC habitats might become less suitable at different locations? It might be OK in the J2 channel but not OK below Overton. Deciding where you want to maintain suitable WC habitat affects sediment augmentation decisions. The EDO needs guidance from the GC on this issue.

## Slide 21: Sediment augmentation to maintain WC habitat (2)
Decision Makers’ Needs | ISAC Comments & Recommendations
EBQ #3. Is sediment augmentation necessary to create and/or maintain suitable WC habitat? | 
 | 3b. Where specifically does Program want to maintain suitable WC habitat? Along the J2 channel? Downstream of Overton? Both?
Notes: The NoSedAug Monitoring Plan shows increases in channel incision WITH sediment augmentation during 2016-2022. Between 2016 and 2022, during active sediment augmentation, the area of incision to 9’ below the floodplain increased from 4.62 to 15.94 acres, which averages out to 1.9 acres / year. WITHOUT sediment augmentation the rate of channel incision is certain to be greater, though year to year fluctuations in flow will be a confounding factor. To make a decision about whether to continue the NoSedAug experiment or whether to resume sediment augmentation, the GC will need decision criteria. How much channel incision to 9’ below the floodplain is unacceptable to the GC in the J2 return channel? 10 acres / year? 100 acres / year? Progression down to the Overton Bridge? Whatever decision criteria are established by the GC, with guidance from the EDO, the EDO will need to provide the GC with some estimate of their level of confidence that thresholds have been exceeded. The costs of restoring sediment augmentation will need to consider filling in the divot created by the NoSedAug experiment.
The Monitoring Plan indicates that the EDO plans to compare the NoSedAug experiment with MechSed. To do this, the EDO will need to filter out the effects of year to year variation in flow. The NoSedAug Monitoring Plan briefly discusses this, but it’s worth discussing this comparison in more detail.

## Slide 22: Sediment augmentation to maintain WC habitat (3)
Decision Makers’ Needs | ISAC Comments & Recommendations
EBQ #3. Is sediment augmentation necessary to create and/or maintain suitable WC habitat? | 
 | 3c. Use EDO’s dynamic approach to tracking annual need for augmentation and amount of sediment required. Look at sub-reach sediment budgets rather than all of J2 reach.
 | .
Notes: 3c. The ISAC likes the dynamic approach recommended by the EDO to track the annual need for augmentation and the amount of sediment required.
It would be useful to estimate the sediment annually supplied from the North Channel, and how that compares to the deficit from the J2 channel. If there’s enough sediment being supplied from the North Channel, then you may not need to worry about incision progressing downstream of Overton.

## Slide 23: Sediment augmentation to maintain WC habitat (4)
Decision Makers’ Needs | ISAC Comments & Recommendations
EBQ #3. Is sediment augmentation necessary to create and/or maintain suitable WC habitat? | 
 | 3d. ISAC thinks the sand dam proposal would decrease, not increase sediment transport. Instead, examine sediment supplied by N. channel and by lateral migration of S. channel.
Notes: 3d. Preliminary HEC-RAS modeling found that the sand dam would cause a net decrease in sediment transport capacity. The North Channel is likely the dominant source of sediment to the Platte near Overton, though more data on sediment budgets and flux are needed.
The ISAC has 3 other concerns about the sand dam proposal, as described in our report from the October 2023 ISAC meeting:
the very rough nature of the connecting channel might entirely preclude sediment arriving in the J2 in the short-term without substantial channel clearing;
it could cause knickpoint propagation and subsequent incision in the North Channel; and
downstream propagation of incision past Overton appears to have been prevented by direct sediment augmentation, a method with far less uncertainty than the sand dam proposal.

## Slide 24: Factors influencing WC decisions to stop in AHR (1)
Decision Makers’ Needs | ISAC Comments & Recommendations
EBQ-4. What factors influence WC decision to stop or fly over the AHR? Does flow matter? Should flow be used when birds are here to increase stopovers, or when birds are not here to maintain channel widths? | 4a. Number of telemetered WCs will be declining. IF you want to assess WC responses to flow and other factors, THEN next few migration seasons will offer best opportunity.
Notes: EBQ-4 asks “What factors influence WC decision to stop or fly over the AHR?” Related decision questions include: “Does flow matter? Should flow be used when birds are here to increase stopovers, or when birds are not here to maintain channel widths?”
Which strategy is more likely to improve WC use of the AHR?
4a. The number of telemetered WCs will be declining. It will become increasingly difficult to test the effect of managed or natural flows on WC stopovers. The next few years will offer the best opportunity to assess WC responses to flow and other factors.

## Slide 25: Factors influencing WC decisions to stop in AHR (2)
Decision Makers’ Needs | ISAC Comments & Recommendations
EBQ-4. What factors influence WC decision to stop or fly over the AHR? Does flow matter? Should flow be used when birds are here to increase stopovers, or when birds are not here to maintain channel widths? | 
 | 4b. Use existing non-telemetry data as well as telemetry data to address EBQ-4.
Notes: 4b. WC telemetry data has received a lot of attention. The long data set of WC monitoring collected by the Program can also be used to address factors correlated with stopovers, not just the telemetry data. That’s in the Science Plan.

## Slide 26: Factors influencing WC decisions to stop in AHR (3)
Decision Makers’ Needs | ISAC Comments & Recommendations
EBQ-4. What factors influence WC decision to stop or fly over the AHR? Does flow matter? Should flow be used when birds are here to increase stopovers, or when birds are not here to maintain channel widths? | 
 | 4c. Describe the relative strengths of correlations with WC stopovers from all hypothesized factors (e.g., time of day, channel width), not just flow.
Notes: 4c. Flow questions need to be answered with a thumbs up or down for clarity to the GC, AND it’s also important to understand the relative importance of all factors, even if doing so doesn’t easily translate into thumbs up or down answers.

## Slide 27: Factors influencing WC stopover length (1)
Decision Makers’ Needs | ISAC Comments & Recommendations
EBQ-5. What factors influence WC stopover length within the AHR? | 5a. Crane groups can change membership and size over time. Suggest EDO and TAC discuss ways to define groups and stopover length (which may correlate with group size).
Notes: On to EBQ-5. Read EBQ-5. As for the factors affecting stopovers just discussed, decision makers want to know whether water and channel width need to be further managed to support longer stopovers in the AHR.
In our report we noted that crane groups can change membership and size over time. We suggested that the EDO and TAC discuss ways to define groups and stopover length (which may correlate with group size). We’ve since learned that the EDO gives groups a new group ID each day, which is a good thing as this allows for a variety of investigations into the data.

## Slide 28: Factors influencing WC stopover length (2)
Decision Makers’ Needs | ISAC Comments & Recommendations
EBQ-5. What factors influence WC stopover length within the AHR? | 
 | 5b. Do WC’s respond to flow per se or to factors like channel width and water depth?
Notes: 5b. The ISAC thinks it’s important to explore whether WC’s respond to flow per se or to factors like channel width and water depth. This question is in the Science Plan. It’s addressed in a physical process hypothesis which looks at depth and the % of channel < 1 ft depth.

## Slide 29: Factors influencing WC stopover length (3)
Decision Makers’ Needs | ISAC Comments & Recommendations
EBQ-5. What factors influence WC stopover length within the AHR? | 
 | 5c. Why give first roosts greater importance in statistical analyses than later roosts? Don’t use confidence intervals to justify ‘statistical similarity’ (in roost site selection report).
Over to Jennifer
Notes: 5c. The roost-selection report is well-done and should be useful to the Program. We raised two key points in our report. First, is it appropriate to give first roosts great importance in the analysis? A crane might stop at the Platte at a reasonable site and, after flying around the next day, discover a better site. The second roost might result from a more informed decision. The EDO believes that the first roosts are more indicative of stopover decisions, and what you might want to put on the ground to attract WCs to stop. That makes sense. Using the full dataset (first and subsequent roosts) can also be informative, which the EDO plans to do.
JENNIFER TO DISCUSS STARTING HERE
Second, there are some applications of confidence intervals to justify ‘statistical similarity’ which are not good statistical practice.
I think we will discuss this in a lot more detail on Thursday. Here the next few slides have a few ideas for people to ponder until then

## Slide 30: From “08 WC Roost Site Selection Report”
Jennifer
Notes: JENNIFER TO DISCUSS SLIDE
Recall that in the Roost selection report, it is useful to compare the results from the latest analysis to the 2017 and 2019 analyses. Consider the yellow line (UOCW that maximizes the Relative selection ratio for the 2017 analysis) and the red line (corresponding value for the 2024 model)
For the Roost selection report, I recommend the following:
To compare yellow (Baasch et al) and red (EDO) lines, you can
Compute the difference in the relative selection ratio at the two unobstructed channel widths. Then use bootstrapping to compute a CI for the difference (or PI as appropriate).
Redo the entire analysis using a Bayesian approach. Then you can compute these Cis easily. BUT I don’t recommend since you’ve already got publication using the frequentist approach

## Slide 31
For the Roost selection report:
To compare yellow (Baasch et al) and red (EDO) lines, you can compute the difference in the relative selection ratio at the two unobstructed channel widths. Then use bootstrapping to compute a CI for the difference (or PI as appropriate).
Not recommended: Alternatively, redo the analysis using a Bayesian model. I don't recommend since you are comparing the new results to the previously published data and analyses which use the frequentist approach
Jennifer
Notes: JENNIFER TO DISCUSS SLIDE

## Slide 32: Moving forward
What are appropriate uses of the resource selection function model?
Appropriate: for a specific UOCW, what is a 95% CI (or PI) for the Relative Selection Ratio (RSR)?
Can’t do: what is a 95% CI for UOCW when RSR is above 50%?
Can’t do: what is a 95% CI for UOCW around the maximum RSR?
Jennifer
Notes: JENNIFER TO DISCUSS SLIDE
The model doesn’t include uncertainty in UOCW (a predictor) so that’s why it isn’t appropriate to compute Cis for the predictor
In general, you can compute a CI for the RSR (y-axis). You can’t compute a CI for UOCW using this model (x-axis). Most regression-type models don’t allow you to construct a CI for a predictor variable.

## Slide 33: Factors influencing WC stopover length (3)
Decision Makers’ Needs | ISAC Comments & Recommendations
EBQ-5. What factors influence WC stopover length within the AHR? | 
 | 5c. Why give first roosts greater importance in statistical analyses than later roosts? Don’t use confidence intervals to justify ‘statistical similarity’ (in roost site selection report).
Notes: 5c. The roost-selection report is well-done and should be useful to the Program. We raised two key points in our report. First, is it appropriate to give first roosts great importance in the analysis? A crane might stop at the Platte at a reasonable site and, after flying around the next day, discover a better site. The second roost might result from a more informed decision. The EDO believes that the first roosts are more indicative of stopover decisions, and what you might want to put on the ground to attract WCs to stop. That makes sense. Using the full dataset (first and subsequent roosts) can also be informative, which the EDO plans to do.
JENNIFER TO DISCUSS STARTING HERE
Second, there are some applications of confidence intervals to justify ‘statistical similarity’ which are not good statistical practice.
I think we will discuss this in a lot more detail on Thursday. Here the next few slides have a few ideas for people to ponder until then

## Slide 34: Factors influencing WC stopover length (4)
Decision Makers’ Needs | ISAC Comments & Recommendations
EBQ-5. What factors influence WC stopover length within the AHR? | 
 | 5d. Consider the multiple sources of information presented in the roost site selection report when setting or modifying targets for channel widths.
Notes: Lots of work has been done on channel widths over several years, including using multiple explanatory variables both on and off the channel, potential management models, and different landcover layers. It’s a complex problem, and any changes to target widths need to be very carefully considered with multiple lines of evidence and risk assessments.
For example, half of roost observations occurred in channels less than the current target width of 650’. That could be interpreted to mean that there aren’t enough places with suitable channel widths, OR that WCs are OK to roost on sites with channels narrower than 650’.

## Slide 35: Spring vs Fall use of AHR by WCs (1)
Decision Makers’ Needs | ISAC Comments & Recommendations
EBQ-6. Why is spring WC use of the AHR greater than fall WC use? When should water be put down the channel? | 6a. Could address seasonality under EBQ-4 and EBQ-5, then remove this EBQ.
Fig.10 in SoPR
Notes: Read EBQ-6. Managers would like to know if the Platte Program is doing its part to support the recovery of WCs, and whether current management actions are necessary and sufficient. We also understand that stakeholders are interested in EBQ-6 because it affects the timing of water management decisions.
The Program could address seasonality under EBQ-4 and EBQ-5, and then remove this EBQ.

## Slide 36: Spring vs Fall use of AHR by WCs (2)
Decision Makers’ Needs | ISAC Comments & Recommendations
EBQ-6. Why is spring WC use of the AHR greater than fall WC use? When should water be put down the channel? | 
 | 6b. Not clear that use is higher in spring, but year to year variability is increasing. Why?
Fig.10 in SoPR
Notes: It’s not clear that WC use is higher in spring based on the graph of crane use days at the lower right. However, year to year variability appears to be increasing. Why?

## Slide 37: Spring vs Fall use of AHR by WCs (3)
Decision Makers’ Needs | ISAC Comments & Recommendations
EBQ-6. Why is spring WC use of the AHR greater than fall WC use? When should water be put down the channel? | 
 | 6c. The two WC metrics are complimentary and communicate different things. Add Average Length of Stay as another indicator of habitat quality?
Fig.10 in SoPR
Notes: 6c. The adjusted proportion of the population (figure on left side) reflects the relative role of the Platte in the overall WC population, and is scaled to that population. Crane use days (figure on the right side) increase with increases in the overall WC population, and with the attractiveness of AHR habitat for WCs. The two WC metrics are complimentary. The average length of stay in the AHR may be worth considering as an additional indicator of habitat quality.
======extra below======
However, this indicator could be interpreted two different ways. WCs might stay longer because the habitat is very high quality, or they need to stay longer to get enough food in poor quality habitat. Having data on habitat quality is helpful, though that’s not easy to define.

## Slide 38: Effects of Program flow mgmt. on pallid sturgeon (1)
Decision Makers’ Needs | ISAC Comments & Recommendations
EBQ-7. What effect do Program flow management actions to benefit WC, PP, and LT in the central Platte River have on PS use of LPR? | 7a. Objectives 2 and 3 (identify spawning habitat; verify spawning) are beyond capacity of UNL team. Focus on Obj. 1 - factors affecting migration into / out of Platte R and tribs.
Notes: Read EBQ-7. Managers would like to know if there’s any connection between Program water management and the needs of PS in the LPR. They would like UNL’s research to help them with water management decisions.
7a. The UNL Progress Report focused entirely on Objective 1 (factors affecting migration into and out of the Platte, and tribs). That makes sense given the challenges of objectives 2 and 3 (identifying spawning habitat, verifying spawning). The ISAC supports the decision of the EDO and UNL to cease sampling for age-0 sturgeon, but to continue deploying and sampling egg mats to collect embryos for genetic analysis. The Platte Program can rely on the MRRP to catch many age-0 fish (up to 15,000 / year, maybe more in future), as well as recaptures of reproductive females, and genetic analyses to confirm whether reproduction occurred in the Platte. That form of collaboration is already happening – a tagged reproductive female that spent time in the Platte was recaptured in the Lower Missouri River by USGS, and had shed her eggs.

## Slide 39: Effects of Program flow mgmt. on pallid sturgeon (2)
Decision Makers’ Needs | ISAC Comments & Recommendations
EBQ-7. What effect do Program flow management actions to benefit WC, PP, and LT in the central Platte River have on PS use of LPR? | 
 | 7b. Temperature affects PS movement and spawning. Include temperature in HDR hydrologic model, ideally in 2D. How much Program water to change LPR temp by 1oC?
Notes: Temperature affects PS movement and spawning. HDR should include temperature in their hydrologic model, ideally in 2D. Modeling how much Program water would be required to alter LPR temperatures by one degree during the spawning season will provide a reality check on the ability of Program water management to shift temperatures in the LPR.
==== extra comment for TAC / EDO ====
UNL found that movement was strongly correlated with the month. Since daylength is known to affect fish reproductive development, it would be good to replace month with daylength in the UNL statistical analyses.

## Slide 40: Effects of Program flow mgmt. on pallid sturgeon (3)
Decision Makers’ Needs | ISAC Comments & Recommendations
EBQ-7. What effect do Program flow management actions to benefit WC, PP, and LT in the central Platte River have on PS use of LPR? | 
 | 7c. It’s worthwhile continuing passive tracking of PS upstream of Elkhorn River to understand PS responses to flow and temperature, including in Loup River.
Notes: 7c. Maintaining the passive array in the Platte River above the Elkhorn is important to the science needs of the EDO PS Framing Document, more important than continuing larval trawling. Active tracking is beneficial, but may not be feasible.

## Slide 41: Effects of Program flow mgmt. on pallid sturgeon (4)
Decision Makers’ Needs | ISAC Comments & Recommendations
EBQ-7. What effect do Program flow management actions to benefit WC, PP, and LT in the central Platte River have on PS use of LPR? | 
 | 7d. Explore how tribs and LMOR affect discharge and temperature in LPR. Understand past, present and future hydrologic conditions in LPR to explore potential effects on PS.
Notes: 7d. It’s worth exploring how the tribs [Loup River, Elkhorn River and Salt Creek {point to map}] and LMOR affect discharge and temperature in LPR. For example, seasonally high LMOR flows can back-up LPR water at their confluence {point to map}. Indicators of Hydrologic Alteration (IHA) have been used on the Missouri and Yellowstone Rivers to assess how past, present and future flows might affect PS use.

## Slide 42: Effects of predation on piping plovers (1)
Decision Makers’ Needs | ISAC Comments & Recommendations
EBQ-8. How much of an effect does predation have on PP productivity (fledging)? EBQ-9. How effective is Program mgmt. at mitigating losses of PP productivity due to predation? | 8a. Put Program findings in context. How does average 25% loss of productivity to predation compare with Missouri program, and to other peer-reviewed studies?
Figure 11
Notes: Read EBQ 8 and 9.: Lots of effort has gone into understanding the amount of PP mortality caused by predators, and how to reduce the level of predation. Managers would like to know if these monitoring and mitigation efforts are necessary and cost-effective.
It’s helpful to put Program findings in context. How does an average 25% loss of productivity to predators compare with Missouri PPs, and to other peer-reviewed studies?

## Slide 43: Effects of predation on piping plovers (2)
Decision Makers’ Needs | ISAC Comments & Recommendations
EBQ-8. How much of an effect does predation have on PP productivity (fledging)? EBQ-9. How effective is Program mgmt. at mitigating losses of PP productivity due to predation? | 
 | 8b. Will scheduled 2024 evaluation of predator mgmt. examine wider range of factors affecting PP fledging besides nest predation? Compare cost-effectiveness of different predation control measures? Evaluate other options?
Figure 11
Notes: 8b. We understand that the 2024 evaluation that’s under way consider a wider range of factors affecting PP fledging besides nest predation, and will examine the cost-effectiveness of different methods of controlling predators, all of which is good. Building additional off-channel sand pits is one possible “other option” to boost PP productivity and compensate for predation losses.

## Slide 44: Effects of predation on piping plovers (3)
Decision Makers’ Needs | ISAC Comments & Recommendations
EBQ-8. How much of an effect does predation have on PP productivity (fledging)? EBQ-9. How effective is Program mgmt. at mitigating losses of PP productivity due to predation? | 
 | 9a. Data that Program’s collecting should help to answer EBQ-9, even though sand pits vary in their attributes. Start with the simplest possible analyses and then proceed as your small data set allows. Continue to use nest cameras.
Figure 11
Notes: 9a. We understand the EDO plans to start with the simplest analyses to address EBQ-9, which we strongly endorse. Some models under consideration at the SPRS were too complex for the size of data set.
We also recommend continuing to use nest cameras to identify nest fates. You can then assess the usefulness of predator cameras based on existing data.

## Slide 45: Wet meadows research (1)
Decision Makers’ Needs | ISAC Comments & Recommendations
EBQ-10. Wet meadows research | 10a. Finish peer-review process. Converge to final GC-approved product.
Notes: EBQ-10 relates to wet meadows research. Lots of research was done on wet meadows. The GC would like to know if WCs need more wet meadows, and if so is it cost-effective to create more of these habitats?
We concur with the current plan to finish the peer-review process and converge to a final GC-approved product.

## Slide 46: Wet meadows research (2)
Decision Makers’ Needs | ISAC Comments & Recommendations
EBQ-10. Wet meadows research | 
 | 10b. Given what you’ve learned, is it worth evaluating mechanical sculpting of wet meadows topography at existing / potential sites? Or would benefits not justify costs?
Notes: Given what the Program has learned, and the various tools developed by EDO staff, some of which are shown on this slide, is it worth evaluating mechanical sculpting of wet meadows topography at existing / potential sites? Or would the benefits not justify costs?

## Slide 47: Thanks for listening! Happy to answer your questions…
Notes: Overall, the ISAC was impressed with the progress made by the Program, and liked the succinct synthesis in the SoPR. We have more detailed comments in our report.