## Slide 1: Sed Aug 2023 Report Peer Review Libby Casavant, P.E.
Types of Feedback
Report Organization
Text/Figure Edits
Analysis and Methods
Notes: Received comments in late spring from Richard Williams, James Brasington and Mark Smith.
Comments/suggestions regarding organization, text/figure edits, analysis, methods. 109 row matrix

## Slide 2
Analysis and Methods Main Topics
Lateral Erosion Delineation Method
Analyze the North Channel as a Control Reach
Volume Change Analysis
LiDAR and Raster Differencing Uncertainty

## Slide 3
Lateral Erosion Delineation Method
Proposed Response: Test manual interpretation on a small reach, compare visually and quantify volumes. Judge which method is more suitable.
Current approach: Hydraulic Model Result Differencing at 5,000 cfs.
Reviewer Comments: Compare to manual interpretation
Notes: We expect differences, and anticipate manual may be more accurate. However, it isn’t very repeatable and could be differences among people. What level of difference is acceptable in exchange for a much less labor intensive, repeatable process?

## Slide 4
Analyze the North Channel as a Control Reach
Proposed Response: Very different hydrology on north channel makes it a poor control reach, so this will not be included in the report.
North Channel
J2 Channel
Overton Bridge
Current approach: Morphology analyzed on J2 Channel only.
Reviewer Comments: Analyze north channel morphology as a “control reach”.

## Slide 5
Volume Change Analysis
Proposed Response: Currently unclear of benefit, but open to providing. Maybe providing more differenced raster figures is helpful?
Current approach: Present net volumetric changes.
Reviewer Comments: Provide raw values of aggradation and degradation.
-20 to -2
-2 to -0.6
-0.6 to -0.001
0
.001 to 0.6
0.6 to 2
2 to 20
Elevation Change (ft)

## Slide 6
LiDAR and Raster Differencing Uncertainty
Systematic or Normal Error?
Threshold to Remove Uncertainty?
LiDAR error is estimated every year by contractor. Typically +/- a few inches
Notes: There is some error in LiDAR data.
Gets reported every year by contractor.
Could deal with this by removing everything uncertain
If don’t threshold, one of the most important things know if the small (erroneous change) is systematic or not. We think ours mostly is, but must quantify to what degree
Small systematic error over large area adds up

## Slide 7
LiDAR and Raster Differencing Uncertainty
Proposed Response:
  Thresholding/ No Thresholding Comparison
  Systematic error testing
  Methodological details
Current approach: No thresholding, all data used
Reviewer Comments: More details and error quantification needed to backup this approach
Notes: Uncertainty in raster data.
Current approach relied on removal of systemic error then use all data. Avoid other techniques like thresholding

## Slide 8
LiDAR and Raster Differencing Uncertainty
  Thresholding/ No Thresholding Comparison
Difference raster with GCD thresholding
Difference raster without thresholding
-20 to -2
-2 to -0.6
-0.6 to -0.001
0
.001 to 0.6
0.6 to 2
2 to 20
Elevation Change (ft)
Notes: Remove any change that is within our uncertainty bounds. W
Re-calculate volume change
compare the results to those presented in our report.
Expected disadvantage: may introduce systematic error.
This may occur because aggradational processes tend to happen at small magnitudes compared to erosion (especially lateral erosion). Therefore, thresholding will remove more bed aggradation than erosion, shifting the balance of our results.
Figure 2021-2020. Values from -0.4 to 0.3 are null in thresholded version. Typical for GCD process and LiDAR wet/dry specs. Assumed spatially consistent error between we/dry

## Slide 9
Chart: Station(ft)
LiDAR and Raster Differencing Uncertainty
2019-2016 | 
MAX | 0.06
MIN | -0.11
AVE | -0.04
MED | -0.04
  Systematic Error Testing
Notes: Something we really need to quantify. Expect error to be normally distributed
See fig- may not always be the case
If presenting raw change, small systematic error over large area adds up.

## Slide 10
LiDAR and Raster Differencing Uncertainty
  Methodological details
Wingtra
NVS Point Cloud
NVS Ground Survey
Notes: We will present a more thorough description of how the LiDAR contractor collected, verified, and post-processed the data.

## Slide 11
In Summary
Lateral Erosion Delineation Method-
Test manual method
Analyze the North Channel as a control reach-
Do not plan to do
Volume Change Analysis-
Present Agg/Deg Totals? Show more figures?
LiDAR and Raster Differencing Uncertainty-
Thresholding, systematic error, contractor methods
  ddd
  k